## Slide 1: PHDL Printed Circuit Board Hardware Description Language
Brent Nelson, Brad Riching, Richard Black
Dept. of Electrical and Computer Engineering
Brigham Young University
October 25, 2011

## Slide 2: Acknowledgements
Pete Dudley – Sandia
  Ideas, motivation, and passion for this project
Wes Landaker - Sandia
  Ideas, language design, compiler consulting
Sandia Management
  Funding

## Slide 3: Overview
Who are we?
What is PHDL? (a very short intro)
Examples of PHDL
  Example board designs
    Language and grammar
    Tool flow
What is PHDL? (more in-depth)
  Why textual input?

## Slide 4: Who Are We?
Dr. Brent Nelson
  Brigham Young University, Dept. of Electrical and Computer Engineering
Brad Riching
  MS Student in Computer Engineering
  BS in Electrical Engineering, Brigham Young University, 2010
Richard Black
  Undergraduate in Computer Engineering, Brigham Young University

## Slide 5: What is PHDL?
Schematic Capture produces netlist
PCB Layout interprets netlist
Bill of Material, other ancillary data
netlist

## Slide 6: What is PHDL?
Schematic Capture produces netlist
PCB Layout interprets netlist
PHDL Source Code
PHDL compiler
Bill of Material, other ancillary data
netlist
netlist

## Slide 7: What is PHDL? (a very short intro)
An HDL for PC Boards
  Hardware Description Language
  For schematic entry (not layout)
Similar to HDLs for IC and FPGA design
  Verilog, VHDL, etc.
Goal == significantly increase:
  Productivity
  Collaboration
  Reuse

## Slide 8: Why PHDL? (the short version)
Automation & productivity
  Iteration, hierarchy, ERC/DRC
Collaboration
  SCCS (source code control system)
    Shared repository for designs and part libraries
    Design versions, change tracking/documentation
    Diff, revert
Textual IDEs and tools
  Templates, auto-completion, search and replace, library reuse

## Slide 9: High Pin Count Devices - FPGAs
How much of this schematic is meaningful?
Most circuit context is absent.
Many pins map to devices on other pages.
Larger devices must be split across multiple pages
Schematics don’t scale well.
HDL’s do!

## Slide 10: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 11: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 12: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 13: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 14: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 15: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 16: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 17: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 18: Trivial Example
We’ll illustrate some of the features of PHDL with an example:

## Slide 19: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 20: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 21: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 22: Creating a Design
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
R?
M0805
1
2

## Slide 23: Creating a Design
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
R?
M0805
1
2

## Slide 24: Creating a Design
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
R?
M0805
1
2

## Slide 25: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 26: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 27: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 28: Creating a Design
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “SA08-21”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
2
15
13
11
5
3
14
10
4
12
17
SA08-21
LD?

## Slide 29: Creating a Design
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “SA08-21”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
2
15
13
11
5
3
14
10
4
12
17
SA08-21
LD?

## Slide 30: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 31: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 32: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 33: Creating a Design
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;

## Slide 34: Creating a Design
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;

## Slide 35: Creating a Design
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;

## Slide 36: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 37: Creating a Design
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;

## Slide 38: Creating a Design
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;

## Slide 39: Creating a Design
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;

## Slide 40: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 41: Creating a Design
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;

## Slide 42: Creating a Design
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;

## Slide 43: Creating a Design
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;

## Slide 44: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 45: Creating a Design
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;

## Slide 46: Creating a Design
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;

## Slide 47: Creating a Design
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;

## Slide 48: Creating a Design
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;

## Slide 49: PHDL Example Design
design ssControl is
device Resistor is
attr refPrefix = “R”;
attr pkg_type = “M0805”;
pin a = {1};
pin b = {2};
end device;
device Switch is
attr refPrefix = “SW”;
attr pkg_type = “MS243”;
pin a = {1}; pin b = {2};
end device;
device Battery is
attr refPrefix = “G”;
attr pkg_type = “1V60R”;
attr value = “9V”;
pin pos = {2}; pin neg = {1};
end device;
device SevenSeg is
attr refPrefix = “LD”;
attr pkg_type = “MS243”;
pin[1:8] segments = {2,15,13,11, 5,3,14,10};
pin[1:3] anode = {4,12,17};
end device;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 50: PHDL Example Design
design ssControl is
include “parts.phdl”;
net gnd, vcc;
net[1:8] segs, r2sw;
begin
inst source of Battery is
pos = vcc;
neg = gnd;
end inst;
inst segment of SevenSeg is
segments = segs;
anode = <vcc>;
end inst;
inst(1:8) swArray of Switch is
combine.a = r2sw;
combine.b = segs;
end inst;
inst(1:8) rArray of Resistor is
newattr value = “120”;
combine.a = r2sw;
each.b = gnd;
end inst;
end design;

## Slide 51: How PHDL Works
Lexer
Parser
PHDL source
Tree Parser
Abstract Syntax Tree (AST)
Analyzer / Generator
Command line switches
Output files
ANTLR framework
Netlist
Bill of Materials
Component List
Layout Directions
XML
Tool-specific Scripts
~/user/brad/phdl/projects
$java phdl.Compile <file_name>.phdl [switches]

## Slide 52: Targeted Design Flows
EAGLE PCB
Mentor Graphics PADS
AD9739 High Speed DAC FMC board – Pete Dudley
FPGA-based Motor Controller - BYU

## Slide 53: BYU Proof of Concept Board
FPGA-based motor controller (2-axes)
  Spartan3 400K 144-pin QFP implements:
    32-bit position, vel. and accel. registers per axis
    Programmable PID filters, sampling intervals
    Trapezoidal velocity profile generators
    Packet router over RS232 to host PC application
  Supporting hardware
    500+ CPR encoder feedback resolution
    PWM brushless and brushed motor drives
    The usual JTAG, Flash ROM, GPIO, etc.

## Slide 54: Motor Controller Board
RS232 Host Application
MOTOR DRIVERS
Single Axis Block Diagram
FPGA VHDL
Hardware Outside FPGA

## Slide 55: Motor Controller Board
Final Layout in EAGLE

## Slide 56: Motor Controller Board
Back From Manufacturing

## Slide 57: Motor Controller Board
Assembled
Top
Bottom

## Slide 58: Motor Controller Board
First PCB Built using PHDL

## Slide 59: Motor Controller Board
Power Supply
12VDC IN:
To 5V, 3.3V, 2.5V, 1.2V
RS232
JTAG
Motor Power 58VDC MAX
Brushless Drive (x2)
Brushed Drive (x2)
Encoder Feedback

## Slide 60: Motor Controller Board
Host Application Interface (C#)
Positioning
Commands
Reporting Commands
Serial Config
Internal State Registers
Raw Data Monitoring

## Slide 61: Automatic Device Generation
library ieee;
use ieee.numeric_std.all;
use ieee.std_logic_1164.all;
entity fpga is
port(
clk : in std_logic;
rst : in std_logic;
-- RS232 serial ports
rxd : in std_logic;
txd : out std_logic;
rxd_a : in std_logic;
txd_a : out std_logic;
-- 12-bit DAC
sclk : out std_logic;
sync : out std_logic;
sdata : out std_logic
data : out std_logic_vector(7 downto 0)
.
.
.
);
end entity fpga;
Synthesis, PAR,
csv2phdl
#fpga.ucf
LOC “clk” = P52;
LOC “rst” = P40:
LOC “rxd” = P47;
LOC “rxd_a” = P41;
.
.
.
Location Constraints
FPGA VHDL Design
device fpga is
attr refPrefix = "U";
attr pkg_type = "tq144";
attr mfgr = "XILINX";
attr partNumber = "xc3s400-4tq144";
// User I/O pins.
pin clk = {P52};
pin rst = {P40};
pin rxd = {P47};
pin rxd_a = {P41};
pin txd = {P46};
pin txd_a = {P44};
pin sclk = {P86};
pin sdata = {P87};
pin sync = {P85};
pin[7:0] data = {P23,P21,P20,P18...};
.
.
.
end;
PHDL Device Declaration

## Slide 62: Automatic Device Generation
Automated FPGA Device Declaration from HDL
fpga.vhdl
fpga.ucf
Synthesis, PAR
fpga.csv
fpga.phdl
csv2phdl
Revisions
design myDes is
include “fpga.phdl”;
begin
…
end design;
PHDL Source Code
PHDL Device Declaration
HDL

## Slide 63: Motor Controller Board
FPGA Instance
inst fpga_inst of fpga is
newattr libName = "xilinx_devices";
partnumber = "122-1717-ND";
newattr supplier = "DIGI-KEY";
newattr cost = "21.95";
// Signal pins from FPGA design.
clk = clk;
rst = rst;
rxd = rxd;
rxd_a = rxd_a;
txd = txd;
txd_a = txd_a;
sclk = sclk;
sdata = sdata;
sync = sync;
data = data;
.
.
.
end;

## Slide 64: Motor Controller Board
~1200 lines of PHDL (25 pages of code)
30 device declarations
  6 library files
672 nets

## Slide 65: Motor Controller Board
Bill of Materials (CSV)

## Slide 66: The Group Construct
group "SWITCHES" is
inst fpga_switches of dipswitch is
a = <vcco>;
b = sw_res;
end;
inst(7:0) sw_pulldown of R0603 is
value = "4.7k";
partNumber = "P4.7KGCT-ND";
combine.a = sw_res;
each.b = gnd;
end;
inst(7:0) sw_lim of R0603 is
value = "4.7k";
partNumber = "P4.7KGCT-ND";
combine.a = sw_res;
combine.b = sw;
end;
end;
Group name
Initial Arrayed Layout

## Slide 67: Why PHDL? (the longer version)
Open format
  Any text tools can read and manipulate
  Design files do not get corrupted
  Easily shared, exchanged, emailed
  Design files forward/backward compatible across tool revisions

## Slide 68: Why PHDL?
IDEs
  Templates and auto completion
  Color syntax highlighting
  Search, search-and-replace
  Scripting
Example: Eclipse

## Slide 69: Why PHDL?
SCCS (source code control system)
  Shared repository for designs and part libraries
  Design versions, change tracking/documentation
  Diff, revert
Collaboration
Reusability
Cross probing

## Slide 70: Why PHDL?
Hierarchy
Focus on functionality rather than looks of schematic
Easy to mis-wire in graphics
  Rats nests
  Missed endpoints
  High pin count packages span multiple pages
  Dangling wires across schematic pages
Non-electrical parts trivial to add

## Slide 71: Why PHDL?
Automation
  Higher level constructs
  Arrays, hierarchy
  Refdes handling
  DRC available to user due to open format
  Lint-like tools easily written
Automatic generation of design files
  Example: device generation from UCF file for FPGAs

## Slide 72: What’s Next?
PHDL 2.0
  Hierarchy support
  Pin directions and DRC
  IDE Eclipse plugin
    Instance template generator
    Syntax coloring
    Content assist
    Hierarchy browser
    Refactoring
  Additional tool flows