PHDL
Schematics Are Dead

---
Electronic SubSystem Development
Electronic SubSystem Development
Work Components
A+
A
C-

---
Software
Quality and Productivity
Software
Quality and Productivity
Increased Abstraction
  - High level language compilers
  - Structured design
  - OO Programming
  - UML, etc
- Code Re-Use/Portability
  - Structured Design
  - OO
  - Open Source, Gnu, Linux, Posix, …
- Revision Management
  - Subversion SVN
  - GIT
  - SourceForge.net, RepositoryHosting.com, Amazon EC2, The Cloud

---
Programmable Logic
Quality and Productivity
Programmable Logic
Quality and Productivity
Increased Abstraction
  - High level languages – VHDL, Verilog, System Verilog, System-C, JHDL, …
  - Structured design
- Code Re-Use/Portability
  - Structured Design
  - OpenCores.Org, Amba, Wishbone, …
- Revision Management
  - Subversion SVN
  - GIT
  - SourceForge.net, RepositoryHosting.com, Amazon EC2, The Cloud

---
Printed Circuit Design
Quality and Productivity
Printed Circuit Design
Quality and Productivity
Increased Abstraction – Blocked!
  - schematic methodology – very low level
  - Each pin on each chip must be handled separately.
- Code Re-Use/Portability – Blocked!
  - proprietary file formats
  - No standards
  - You cannot even read my source without special software
  - Designs not portable even between versions of the same tools
  - In truth, graphical schematics are re-entered manually, over and over
- Revision Management – Blocked!
  - Binary file formats
  - You never know what happened, just “File Changed”!

---
Design
Design
Refactor
Step 1
Step 2
Step 3
Advance

---
PCB Software
That Which Was Difficult is Now Easy
That Which Was Easy is now Difficult
- Physical Layout software has improved dramatically
- Schematic software has worsened dramatically
- Why?
  - Vendor Lock-In
  - Total Customer Dependency
- Mentor controls us.
- Mentor owns our IP.
Define
Connectivity
Netlist
Physical
Layout

---
Problems with Schematic Entry
Problems with Schematic Entry
- Difficult to learn and relearn
- High ratio of non-productive to productive activities.
  - Installation
  - Training
  - Retraining
  - Bug reporting
  - Tech support interaction
- Incompatible with version control
  - Not suitable for important designs.
- Graphical Tool for non-graphical problem
- Maximizes number of manual tasks and opportunities for error.
- Not abstract
  - Each pin must be handled individually
  - Don’t scale well to complex designs
- Not under our control – Mentor Corporation owns us.
- Buggy software
- Not portable
- Very Expensive
- Very Slow
- Very Error Prone
- Inhumane

---
Schematic Capture
productive vs. non-productive work
Schematic Capture
productive vs. non-productive work
work breakdown

---
Schematics
Schematics
Click to edit Master text styles
Second level
Third level
Fourth level
Fifth level

---
Schematics Don’t Scale Well
Schematics Don’t Scale Well
Click to edit Master text styles
Second level
Third level
Fourth level
Fifth level

---
Schematics Don’t Scale Well
Schematics Don’t Scale Well
Click to edit Master text styles
Second level
Third level
Fourth level
Fifth level

---
Typical Schematic Error
Typical Schematic Error
Click to edit Master text styles
Second level
Third level
Fourth level
Fifth level

---
What is PHDL?
What is PHDL?
- A super simple Hardware Description Language (HDL) for PCB connectivity definition.
- An Application Specific Language (ASL).
- Written by Brad Riching, Richard Black and Dr. Brent Nelson at BYU.
- Sandia research contract funded by Steve Becker and Brett Remund.
- Compiler is Java application – runs on all computers.
- Uses Antlr parser generator for syntactical flexibility.
- Free – Open Source project http://phdl.sourceforge.net/

---
PHDL Advantages
(over schematic entry)
PHDL Advantages
(over schematic entry)
- Create and maintain with any text editor. (Vim has context sensitive highlighting.)
- Success promoting syntax - Reduces rate of design errors.
- Compatible with version control.
- No obstacles to re-use.
- Provides abstraction of signals and components. (Soon will provide hierarchical design.)
- Good error reporting and design rule checking at compile time.
- Supports text-to-text auto-generation – Xilinx to PHDL converter exists.
- Multiple output formats.
- Easy to learn.
- Minimizes typing, fiddling and fighting.
- Java app – runs on all operating systems.
- Open Source and free!

---
Click to edit Master text styles
Second level
Third level
Fourth level
Fifth level

---
Connectivity Definition
(two steps)
Connectivity Definition
(two steps)
- Define your components
- Wire them up

---
Automated FPGA Component Declaration
Automated FPGA Component Declaration

---
Component Declaration
(auto-generated)
Component Declaration
(auto-generated)
//PART TYPE = xc6vlx75t
//SPEED GRADE = -2
//PACKAGE = ff784
//INPUT FILE = fmcw_fpga_pad.csv
//Root Filename = fmcw_fpga
//Full Part Number = xc6vlx75t-2ff784
// Device declaration extracted from Xilinx fmcw_fpga_pad.csv
device fmcw_fpga is
attr refPrefix = "U";
attr pkg_type = "ff784";
attr mfgr = "XILINX";
attr partNumber = "xc6vlx75t-2ff784";
// User I/O pins.
pin adc_cal = {Y22};
pin adc_caldly = {T25};
pin adc_calrun = {T24};
pin adc_dclk_rst_n = {D11};
pin adc_dclk_rst_p = {E12};
pin adc_dclki_n = {AE10};
pin adc_dclki_p = {AF10};
pin adc_dclkq_n = {AE14};
pin adc_dclkq_p = {AD13};
pin adc_ddrph = {V24};
pin adc_des = {W22};
pin[11:0] adc_di_n = {J23,J27,AB7,AA10,A27,G16,J22,F12,G26,B28,E14,F24};
pin[11:0] adc_di_p = {K24,J26,AA7,Y10,A26,H16,J21,G12,G27,B27,E13,E25};
pin[11:0] adc_did_n = {Y9,D15,F17,K18,B13,D21,D12,F21,G21,B23,A25,J20};
pin[11:0] adc_did_p = {W8,E15,G17,K17,C14,E20,D13,F20,H20,B22,A24,K19};
pin[11:0] adc_dq_n = {C21,C11,C20,A22,E19,F25,K23,E27,A19,H15,E28,G24};
pin[11:0] adc_dq_p = {B21,B11,C19,A21,D20,F26,K22,F27,A20,J16,D28,H24};
pin[11:0] adc_dqd_n = {G9,D25,G19,H28,F19,E17,A12,B19,H18,D18,A16,J18};
pin[11:0] adc_dqd_p = {G8,E24,H19,G28,E18,D17,A11,B18,G18,C18,A15,J17};
…

---
Component Declaration
(auto-generated)
Component Declaration
(auto-generated)
…
pin DXP_0 = {T14};
pin[169:0] GND = {A1,A18,A2,A28,A6,A8,AA1,AA18,AA2,AA28,AA5,AA8,AB15,AB25,AB3,AB5,AC1,AC12,AC22,AC5,AC6,AD19,AD3,AD4,AD5,AD9,AE1,AE16,AE26,AE5,AE6,AF13,AF23,AF3,AF5,AG1,AG10,AG20,AG5,AH17,AH27,AH3,AH5,AH7,B15,B25,B3,B4,B6,C1,C12,C22,C5,D19,D3,D5,D9,E1,E16,E26,E5,E6,F13,F23,F3,F5,G1,G10,G2,G20,G5,H17,H27,H3,H4,H5,H7,J1,J14,J2,J24,J5,K11,K21,K3,K5,K6,L1,L10,L12,L14,L16,L18,L28,L5,L8,M11,M13,M15,M17,M25,M3,M5,M9,N1,N10,N12,N16,N18,N22,N5,N6,N8,P11,P15,P17,P19,P3,P7,P9,R1,R10,R12,R16,R18,R26,R5,R6,R7,R8,T11,T15,T17,T19,T23,T3,T4,T7,T9,U1,U10,U12,U14,U16,U18,U20,U5,U6,U7,U8,V11,V13,V15,V17,V27,V3,V5,V6,V7,V9,W1,W14,W2,W24,W5,W6,Y11,Y21,Y3,Y5};
pin HSWAPEN_0 = {N7};
pin INIT_B_0 = {M6};
pin M0_0 = {F6};
pin M1_0 = {D6};
pin M2_0 = {C6};
pin[9:0] MGTAVCC = {AB4,AF4,AH4,D4,F4,K4,M4,P4,V4,Y4};
pin[8:0] MGTAVTT = {AC2,AE2,AG2,C2,E2,L2,N2,R2,U2};
…
pin VN_0 = {R13};
pin VP_0 = {P14};
End device;
Powers and grounds are handled as
Single pins with associated pin
Number lists.

---
Power Connection
(at component instantiation)
Power Connection
(at component instantiation)
Design big_design is
net GND, +2V5, MGTAVCC, MGTAVTT;
…
Begin
Inst big_fpga of fmcw_fpga is refDes=“U1”;
…
…
GND = <GND>;
HSWAPEN_0 = +2V5;
INIT_B_0 = INIT_B_0;
M0_0 = GND;
M1_0 = +2V5;
M2_0 = GND;
MGTAVCC = <MGTAVCC>;
MGTAVTT = <MGTAVTT>;
…
…
End inst;
…
…
End design;
1 line power and ground
Connections are nearly impossible
To mess up.

---
PHDL in Version Control
PHDL in Version Control

---
Example Design
Example Design
Click to edit Master text styles
Second level
Third level
Fourth level
Fifth level
2.5Gs/s DAC Board
FMC format (for ML605 carrier only)
Captured in PHDL
Physical layout in Mentor PADS

---
Device Declaration
Device Declaration
// Analog Devices high speed DAC
device ad9739 is
    attr refPrefix = "U";
    attr refDes = "";
    attr name = "";
    attr value = "";
    attr pkg_type = "ANALOG_DEVICES_BC-160-1";
    attr mfgr = "Analog Devices";
    attr PartNumber = "AD9739BBCZ";
    attr cost = "70.00";
    pin[1:8] VDDC = {C1, C2, D1, D2, E1, E2, E3, E4};
    pin[1:14] VSSC = {A1, A2, A3, A4, A5, B1, B2, B3, B4, B5, C4, C5, D4, D5};
    pin[1:8] VDDA = {A10, A11, B10, B11, C10, C11, D10, D11};
    pin[1:8] VSSA = {A12, A13, B12, B13, C12, C13, D12, D13};
    pin[1:18] VSSA_SHIELD = {A6, A9, B6, B9, C6, C9, D6, D9, F1, F2, F3, F4, E11, E12, E13, E14, F11, F12};
    pin NC = {A14};
    pin[1:4] IOUTN = {A7, B7, C7, D7};
    pin[1:4] IOUTP = {A8, B8, C8, D8};
    pin I120 = {B14};
    pin VREF = {C14};
    pin IPTAT = {D14};
    pin DACCLK_N = {C3};
    pin DACCLK_P = {D3};
    pin IRQ = {F13};
    pin RESET = {F14};
    pin CS = {G13};
    pin SDIO = {G14};
    pin SCLK = {H13};
    pin SDO = {H14};
    pin[1:4] VDD33 = {J3,J4,J11,J12};
    pin[1:6] VDD = {G1, G2, G3, G4, G11, G12};
    pin[1:10] VSS = {H1, H2, H3, H4, H11, H12, K3, K4, K11, K12};
    pin SYNC_OUT_P = {J1};
    pin SYNC_OUT_N = {J2};
    pin SYNC_IN_P = {K1};
    pin SYNC_IN_N = {K2};
    pin DCO_P = {J13};
    pin DCO_N = {J14};
    pin DCI_P = {K13};
    pin DCI_N = {K14};
    pin[13:0] DB1_P = {L14,L13,L12,L11,L10,L9,L8,L7,L6,L5,L4,L3,L2,L1};
    pin[13:0] DB1_N = {M14,M13,M12,M11,M10,M9,M8,M7,M6,M5,M4,M3,M2,M1};
    pin[13:0] DB0_P = {N14,N13,N12,N11,N10,N9,N8,N7,N6,N5,N4,N3,N2,N1};
    pin[13:0] DB0_N = {P14,P13,P12,P11,P10,P9,P8,P7,P6,P5,P4,P3,P2,P1};
end device;

---
Device Instantiation
Device Instantiation
    // This the fast DAC itself. Note how concisely the busses are connected.
    inst fast_dac of ad9739 is refDes = "U1";
        VDDC = <+1V8>;
        VSSC = <gnd>;
        VDDA = <+3V3>;
        VSSA = <gnd>;
        VSSA_SHIELD = <gnd>;
        NC = open;
        IOUTN = <IOUTN>;
        IOUTP = <IOUTP>;
        I120 = I120;
        VREF = DAC_VREF;
        IPTAT = IPTAT;
        DACCLK_N = DACCLK_P; // clock polarity reversed for better routing.
        DACCLK_P = DACCLK_N;
        IRQ = IRQ;
        RESET = RESET;
        CS = SPI_CS;
        SDIO = SPI_SDI;
        SCLK = SPI_SCLK;
        SDO = SPI_SDO;
        VDD33 = <+3V3>;
        VDD = <+1V8>;
        VSS = <gnd>;
        SYNC_OUT_P = SYNC_OUT_P;
        SYNC_OUT_N = SYNC_OUT_N;
        SYNC_IN_P = SYNC_IN_P;
        SYNC_IN_N = SYNC_IN_N;
        DCO_P = DCO_P;
        DCO_N = DCO_N;
        DCI_P = DCI_P;
        DCI_N = DCI_N;
        DB1_P = DB1_P;
        DB1_N = DB1_N;
        DB0_P = DB0_P;
        DB0_N = DB0_N;
    end inst

---
Include Statement and
Signal Declaration
// This board design implments an FMC card that contains a wide-band
// DAC for the synthesis of radar waveforms. The FMC card is intended to
// be installed on a Xilinx ML605 evaluation board.
design fmc_dac is
    // device definitions
    include "devices.phdl";
    // Power and ground nets.
    net +3V3, +2V5, +1V8, 1V8_sense, gnd;
    // net VDDC, VDDA;
    // DAC Signals.
    net IOUTP, IOUTN;
    net[13:0] DB1_P, DB1_N, DB0_P, DB0_N;
    net DACCLK_P, DACCLK_N, DCI_P, DCI_N, DCO_P, DCO_N, SYNC_IN_P, SYNC_IN_N, SYNC_OUT_P, SYNC_OUT_N;
    net IRQ, RESET, SPI_CS, SPI_SCLK, SPI_SDO, SPI_SDI;
    net IRQ_2V5, RESET_2V5, SPI_CS_2V5, SPI_SCLK_2V5, SPI_SDO_2V5, SPI_SDI_2V5;
    net DAC_VREF, IPTAT, I120;
    net analog_out;
    // Clock signals.
    net samp_clk_in, bal_clock_p, bal_clock_n, coup_clock_p, coup_clock_n;
    net clock_buf_p, clock_buf_n;
    net ADCLK914_Vref;
    net out_coup_clock_p, out_coup_clock_n;
    // Test signals.
    net test_trace_bottom, test_trace_top;
begin
    // This the fast DAC itself. Note how concisely the busses are connected.
    inst fast_dac of ad9739 is refDes = "U1";
        VDDC = <+1V8>
Include Statement and
Signal Declaration

---
Dichotomy of Importance and Complexity
Dichotomy of Importance and Complexity
- PHDL
- PHDL
- Schematics
- PHDL
- PHDL
Complexity
Importance

---
To Do
To Do
Get the word out.
  - Sandia Presentation October 25th
  - Road Show – Santa Clara, Kuala Lumpur.
- Hierarchical syntax (in progress).
- Simplified looping syntax.
- More output netlist formats including VHDL.

---
Special Thanks
Special Thanks
- Steve Becker - sponsorship
- Brett Remund - sponsorship
- Mike Knoll – sponsorship
- Wes Landaker – tech consulting
- Mike Gardner- tech consulting
- Dr. Brent Nelson – technical leadership
- Brad Riching – compiler design
- Richard Black – compiler design
- Many others – technical ideas

---
Conclusion
Conclusion
- Electronics design is very important.
- The way we do it now is very inefficient.
- It is time to treat hardware design as IP.
- PHDL provides an excellent alternative.
- PHDL leverages quality and productivity techniques developed by the software industry.
- PHDL is free and available today.
- Get involved!
  - http://phdl.sourceforge.net/
  - For more info: pete@HDLGuy.com